## Slide 1: Workshop 1
Basic Hardware & Arduino

## Slide 2: Introduction to Basic Hardware

## Slide 3: Wire Cutter (Fun Fact)
- Wire Cutting
- Removing excess leads from soldered components (obvious)
- Cutting Prototyping Boards
Notes: Talk about Rapid Prototyping. (Arduino and also use of single core wires)

## Slide 4: Wire Stripper (Fun Fact)
- Ease of stripping wires.
- Usually come with wire cutter
- Some wire cutters are “automatic”
Notes: Talk about Rapid Prototyping. (Arduino and also use of single core wires)

## Slide 5: Prototyping Board (Types)
Breadboard
Stripboard
Perfboard

## Slide 6: Prototyping Board (Breadboard)
Benefits:
- Rapid Prototyping
- No Soldering
Limitations:
- Bulky
- Temporary Prototype
Notes: Talk about Rapid Prototyping. (Arduino and also use of single core wires)

## Slide 7: Prototyping Board (Stripboard)
Benefits:
- More Permanent Prototype
- Neat
Limitations:
- Soldering Needed
- Hand Drill Needed to break unwanted but built-in connections
- Some irreversible actions

## Slide 8: Prototyping Board (Perfboard)
Benefits:
- More Permanent Prototype
- Neat
- Extremely flexible
Limitations:
- Soldering Needed
- Need more wires than stripboard

## Slide 9: We will provide you these 3 types of boards
Breadboard
Stripboard
Perfboard

## Slide 10: Soldering

## Slide 11: Soldering Iron (Construction)
Apply your solder wire (solder tin) on the iron tip!

## Slide 12: Soldering Techniques- sequence
Count to 5 second, then release soldering iron

## Slide 13: Soldering Techniques

## Slide 14: Soldering Techniques – Stability
Make sure your prototype board is secured so that it does not move while being soldered!
Use these to secure the prototype board:
- Tape
- Blue tack
- Bent component leg
- Your friend’s hand (careful!!!)

## Slide 15: Soldering Techniques - Stability

## Slide 16: Soldering Iron (How to Clean Your Iron Tip)
Wire Mesh
For better soldering result!
Notes: Talk about using newspaper

## Slide 17: Desoldering

## Slide 18: Desoldering Techniques (Hand Pump)

## Slide 19: Desoldering Techniques (Solder Bridge)

## Slide 20: Troubleshooting Circuit

## Slide 21: Circuit Troubleshooting - Mentality
Step 1: disconnect the power source

## Slide 22: Circuit Troubleshooting - Mentality
Step 2: narrow down to a “functional part” of circuit
X

## Slide 23: Circuit Troubleshooting - Mentality
Step 3: look for visual clue:
Burn
Dangling/loose wires
(Open Circuit)

## Slide 24: Circuit Troubleshooting - Mentality
Step 3: look for visual clue:
-Wrong orientation?

## Slide 25: Circuit Troubleshooting - Multimeter
Continuity test: check whether wire / connection is good

## Slide 26: Circuit Troubleshooting - Mentality
Step 5: Circuit Analysis
Is the voltage there or is the current there? What is the expected value? Is the value correct?

## Slide 27: Introduction to Arduino

## Slide 28: What is ?
World’s leading open-source hardware and software ecosystem
Originally started as a research project at the Interaction Design Institute of Ivrea, Italy
Tool for IoT product development, project prototyping and for STEM education.
ARDUINO UNO

## Slide 29: What is ?
Programs are written in the Arduino Integrated Development Environment (IDE)
Known as “Sketches”
Files (.ino) are uploaded to the Arduino board via USB cable
Software

## Slide 31: Assumption: You know basic concept of programming, such as variables, functions, if else, for loop, while loop, etc.

## Slide 32: Getting Started!
Connect the Arduino board to your computer

## Slide 33
Ensure that “Arduino/Genuino Uno” is selected as the board: Tools > Board > Arduino/Genuino Uno
Getting Started!

## Slide 34: Getting Started!
Ensure that “Arduino/Genuino Uno” is selected as the board: Tools > Port > COM[X] (Arduino/Genuino Uno)

## Slide 35: Getting Started!
void setup()
Segment where variables, pinModes are declared to initialise the Arduino Board and the program
Will run once after each power up or reset of Arduino Board
void loop()
Segment where the actual program is used to actively control the Arduino Board
Board Information
Upload
Upload program to the Arduino Board
Verify
Compile the program and check for errors

## Slide 36: Blinking LED
Objective: To blink the onboard LED.
The code is available at
tinyurl.com/escendo2020

## Slide 37: Reading from a Button
Objective: To detect whether a button is pressed.
Wire up your button like so:

## Slide 38: Reading from a Button
Objective: To detect whether a button is pressed.
The code is available at
tinyurl.com/escendo2020

## Slide 39: This feature is very useful in debugging (e.g. print value of variables, sensor reading, etc.). You can also print texts, e.g. Serial.print(“Hello! I am:”); Serial.println(my_name); The ‘ln’ means going to a new line after printing.
Serial Monitor

## Slide 40: Challenge - Reading from a Button
Try modifying the code so that the button controls whether the onboard LED is on!

## Slide 41: Coding for a specific task can get daunting or tedious! Libraries to the rescue! Basically, we are using codes that others have written and shared, so we don’t have to code from scratch to do a specific task.
Libraries

## Slide 42: Example: Controlling an LED strip. This is very challenging to code from zero! (need to know LED hardware specification, AVR-C, assembly, direct register access, etc.) Using libraries, the complexity is down to just several lines of codes. We’ll use a neat library called FastLED.
Libraries

## Slide 43: Using Libraries: LED Strip
Go to https://github.com/FastLED/FastLED
Click ‘Clone or download’
Click ‘Download ZIP’
DO NOT
unzip the file!

## Slide 44: Adding FastLED Library
To add the library into the Arduino IDE:
Sketch > Include Library > Add ZIP Library
Choose the zip file you downloaded

## Slide 45: LED Strip
Connections:
Objective: to control an LED strip.
GND
5V
Data (Pin 3)

## Slide 46: LED Strip
Objective: to control an LED strip.
The code is available at
tinyurl.com/escendo2020
Try to:
Change color and brightness.
Control all 3 LEDs.
Make a fading effect (hint: for loop and short delay).

## Slide 47: What’s next? Explore!

## Slide 48: Remember, these are your best friends: - Google - Arduino Reference (arduino.cc/reference/en/) - Built-in example codes
Every time you would like to do something new / have problems, Google and online documentation can answer your questions.

## Slide 49
Just kidding… You’re welcome to ask us!

## Slide 50: Thank You Happy Making!